NAND & NOR gates are readily available because they are easy to manufacture
The combination of the two makes it possible to replicate any logical circuit

NAND Implementation:

Inverter → symbol is triangle with open circle
- x - > x’
- two inputs jumpered to one signal

OR
- two inputs
- can be built with NAND gates

AND_invert is essentially NAND
- F = (x.y.z)’

invert_OR
- x’ + y’ + z’ = (x.y.z)’

Function Implementation using NAND Gates:
1) Draw the logic diagram w/ AND & OR Gates, inverters, etc
2) Replace AND with AND_invert or NAND, replace OR gates with invert_OR
3) Compensate for the circles

Ex:
F = AB + A’C + BC’ + C

AB → NAND
→
A’C → NAND	All going to OR gate (If you need the complement just negate output with NAND)
→
BC’ → NAND

C →	→	Need to compensate for circle on C by making it C’

Need to review this in text – pay attention to level of gates

Ex:
F = A(CD + B) + BC’

CD	→ NAND
CD NOR B’
B	→ NAND (compensate for NOR with B’)
A NAND (CD + B’)
A	→ NAND
BC’ NOR (A NAND (CD + B’))
BC’	→ NAND

NOR Implementation:

NOT: jumper a NOR gate
A → (A+A)’ = A’

OR: NOR gate followed by jumpered NOR gate(NOT)
A’
→ (A+B)’	→ (A+B)’’ = A+B
B

AND: two jumpered NOR gates (NOTs) followed by NOR gate
A	->
B	->

OR_invert: 3 inputs to (A + B + C)’

Invert_AND: 3 inputs to (A + B + C)’

NOR Implementation:
1) Draw logic diagram using AND & OR gates
2) Replace OR w/ OR_invert
3) Replace AND w/ invert_AND
4) Compensate for circles

Ex:
F = (AC + DE)(B + D).C

Need to go over k-map stuff – understand how to use it and for what purpose
- Sum of product vs Product of Sums

Ex:
F = (A + B’)(C + D)
Get F’ in 2 level NOR Implementation

F’ = A’B + C’D’
CD→	00	01	11	10
AB
00	0	1	1	1
01	0	0	0	0
11	0	1	1	1
10	0	1	1	1

Exclusive_OR Function: XOR (symbol = + in a circle)
x XOR y = xy’ + x’y
Complement of XOR is always 1

XOR Commutative: A XOR B = B XOR A
XOR Associative: (A XOR B) XOR C = A XOR (B XOR C)

XOR Gates are difficult to fabricate – can construct with other types of gates
x XOR y = xy’ + x’y

Ex:
F	= (A XOR B) XOR C
= (AB’ + A’B) XOR C
= (AB’ + A’B)C’ + (AB’ + A’B)’C
= AB’C’ + A’BC’ + [(A’+B).(A+B’)]C
= AB’C’+A’BC’ + [A’A’ + A’B’ + AB + B.B’]C
= AB’C’ + A’BC’ + A’B’C + ABC

Homework: F = (A XOR B) XOR (C XOR D) ← Truth Table and expanded function

Parity Bit:
Used for error detection during transmission of binary information
Is an extra bit to make # of 1s even or odd

The circuit that generates the parity bit in the transmitter is called the parity generator

The circuit that checks the parity bit in the receiver is called the parity checker

Ex:
3 bit msg

x	y	z	P
0	0	0	0	0
1	0	0	1	1
2	0	1	0	1
3	0	1	1	0
4	1	0	0	1
5	1	0	1	0
6	1	1	0	0
7	1	1	1	1

3 bit msg w/ P → even parity
p → odd function
whenever P = 1 → # of 1s odd
whenever P = 0 → # of 1s even

P = x XOR y XOR z

Ex:
3 bit msg w/ P → destination
parity checker → check for errors
Parity Checker: if # of 1s even → 0 O.K.
Parity Checker: if # of 0s odd → 1 error

3 bit msg w/ Parity: see photos for parity checker truth table