## Slide 1
F o r w a r d K i n e m a t i c s
- DH Method

## Slide 2
The Situation:
You have a robotic arm that starts out aligned with the xo-axis.
You tell the first link to move by 1 and the second link to move by 2.
The Question:
What is the position of the end of the robotic arm?
Solution:
1. Geometric Approach
This might be the easiest solution for the simple situation. However, notice that the angles are measured relative to the direction of the previous link. (The first link is the exception. The angle is measured relative to it’s initial position.) For robots with more links and whose arm extends into 3 dimensions the geometry gets much more tedious.
2. Algebraic Approach
Involves coordinate transformations.

## Slide 3
Denavit - Hartenberg Method

## Slide 4: Why DH
A simple and standard way of representing and modeling robots and their motions.
Find the homogeneous transformation H relating the tool frame to the fixed base frame

## Slide 6
We attach a Cartesian coordinate frame to each link of a robot and determine the position and orientation of each frame with respect to the others. Therefore, to determine the position and orientation of the end effector, we need to find the end-effector frame in the base frame.

## Slide 7: DH Notations
Kinematic Chain from end effector frame Bn to base frame B0
Each joint is assigned to a coordinate frame.

## Slide 8: DH Notation
The base frame is frame 0.
A joint and its rigidly attached link have the same index i.
Motion of link i can be done by moving joints i, (i-1),… not joint (i+1).
The coordinate frame Bi is fixed to the link i and the coordinate frame Bi-1 is fixed to the link (i − 1).

## Slide 9: DH parameters
Link i connects proximal joints i and distal joint (i+1)
Link i connects frame i-1 and frame i
Four link variables of link i
θi joint angel: a variable if joint i is R (revolute)
di joint distance: a variable if joint i is P(prismatic)
  αi is twist angle
  ai is link offset
cannot change unless reconfigure the robot

## Slide 10: DH Notation (repeat)
For n joints: we have n+1 links. Link 0 is the base
Joints are numbered from 1 to n
Frame Bi {Xi Yi Zi} is attached to the end point of link i, link i is controlled by joint i, not joint (i+1)
Variable parameters θi and di for frame i (aka link i) refer to rotation angle and translation distance of joint i, not joint (i+1). (That is why the superscript is i.)
Frame B0 { X0 Y0 Z0} is attached to the robot base (inertial frame).
Read textbook Chapter 5.1 for notation please.

## Slide 12: Translation between two adjacent frames from frame Bi to Bi-1
During these transformations, Bi-1 acts as the global coordinate frame for the local coordinate frame Bi, and these motions are about and along the global axes.

## Slide 13: Translation between two adjacent frames from frame Bi to Bi-1

## Slide 14: Translation between two adjacent frames from frame Bi to Bi-1
If a translation D and a rotation R are along and about the same axis, it does not make a difference to apply D first and then R or vice versa. Therefore

## Slide 16: Rules of assigning frames
Assign Zi-1 to the actuation of joint i.
  Axis of revolution of revolute joint
  Axis of translation of prismatic joint
Assign Xi so that
Derive axis Y from on X and Z following right hand rule.

## Slide 17: Example: DH parameters The two links arm
Base frame O0
All Z axes are normal to the page
link | ai | αi | di | θi
1 | l1 | 0 | 0 | θ1*
2 | l2 | 0 | 0 | θ2*
* variable

## Slide 18: Example: DH parameters The three links arm

## Slide 20: Homogeneous Transformation Matrix for different types of links
Each joint can be P or R; the axes of two adjacent joints can be parallel ||, orthogonal ├, or perpendicular ⊥.
Two orthogonal joint axes ├ interest at a right angle; Two perpendicular joint axes ⊥ are at a right angle with respect to their common normal.

## Slide 21: R||R manipulator
link | ai | αi | di | θi
1 | l1 | 0 | 0 | θ1*
2 | l2 | 0 | 0 | θ2*

## Slide 22: R||R||R

## Slide 23: Orthogonal joints
Zi and Zi-1 are at right angle and are intersecting
Keep in mind: the proximal frame i-1 is the reference (global) frame in the transformation i-1Ti

## Slide 24: Perpendicular joints

## Slide 27: References
Textbook: Theory of Applied Robotics -Kinematics, Dynamics, and Control (2nd Edition). Jazar, Reza N.